## Slide 1: IPAG Overview

## Slide 2: Agenda
Overview
Architecture
Current Services Offered on IPAG
Service Delivery Flow
Service Assurance Flow
Applications Involved
Question & Answers

## Slide 3: Overview
Next Generation IP Based Network IPAG stands for Internet Protocol Aggregation and is the next generation AT&T network architecture. IPAG is replacing legacy Cisco networks. IPAG will provide a substantially more economical, scalable and reliable multi-service Ethernet platform.
IPAG will be substantially more cost effective than present operation.
IPAG network elements and network design are more scalable than the Cisco 7609 architecture, the Juniper MX960 has 3x the capacity of the Cisco 7609.
One of the major benefits will be to the Wireless Industry. Today, the infrastructure supporting these T1 lines is expensive and bandwidth growth potential is very limited. The IPAG network can bring the Ethernet network much closer to the Cell Towers lowering cost of installation and maintenance as well as providing much needed bandwidth to the Cell Towers

## Slide 4: IPAG : Service Delivery

## Slide 5: Service Delivery Flow
Pre-sales
Ordering
Provisioning
ROME – This is eCRM application where customer details is gathered
• PCGLOBES – Pricing details and other network and service related information is captured in PCG.
ASOC – Service availability is done in ASOC.
AERS – This is Business Object from where we can pull the presales report.
• EXACT – This is mainframe based order creation application wherein an ASR ( Access Service Request) is created.
•SOCS/SORD – This is Service order processor (sops) which is used for billing.
• IDIS – This is Inventory Design Integrated Model where order provisioning is done.
• WFA/C – This is Work Force Administration application.
• LPP - This is Logical Provisioning platform in which Service Activation is done.
CRAMER – This stores network inventory details.
TIRKS - It performs the design and sends a Work Order Request Document (WORD) to WFA.

## Slide 6: IPAG : Service Assurance

## Slide 7: IPAG Service Assurance - Overview
Service Assurance is the application of policies and processes by the Service Provider to ensure that services offered over it’s networks meet a pre-defined service quality level for an optimal Consumer experience.
Service Assurance comes into effect as soon as the service (in this case, ASE - AT&T Switched Ethernet) is provisioned to the Consumer. This ensures a win-win situation for both, the Consumer and the Provider; the Consumer gets the best service (value for money) and the Provider gets a Loyal customer, and possibly many more due to word of mouth publicity.
The practice of service assurance enables CSPs to identify faults in the network and resolve these issues in a timely manner so as to minimize service downtime. The practice also includes policies and processes to proactively pinpoint, diagnose and resolve service quality degradations or device malfunctions before subscribers are impacted.
Service Assurance is ensured by using a string of IT applications which work in tandem with the Network Infrastructure. Service Assurance can be divided into below sub categories-
  Fault Management
  Performance Management
  Trouble Ticket Management
  SLA Management
  Customer Network Management
  Change Management

## Slide 8: Manual Ticket Creation In AOTS TM And Diagnose
A Manual Trouble Ticket is opened by the CSR when a Customer calls in to report a trouble.
Initial Diagnose is done by the IT systems on the Network Devices to isolate the trouble.
If Manual intervention is required to fix the issue, Trouble is referred to WFA/C.
AOTS - TM
CBUS
RUBY CC
CTP
LPP INSTAR
NTE/ Aggregator Devices
IPAG/ VPLS (Backbone) Devices
GCP

## Slide 9: External Engagement (Fault Resolution) Flow
If Trouble Reported in AOTS-TM (Manual or Auto) requires a Field Technician to be engaged for resolution, the Trouble Ticket is referred, via EBTA & TM-BIS/CSI (flow thorugh apps) to WFA-C (Work Force Allocation), which in turn engages a Field Technician for Trouble Resolution.
WFA-C can either engage WFA-DI (for issues within the Central Office) OR WFA-DO (for issue outside the Central Office).
NOTE: WFA DO/DI wil be replaced by FORCE in future (WFA-DO has already been replaced).
AOTS TM
WFA/C
EBTA
TMBIS/CSI
WFA/DI
WFA/DO

## Slide 10: Alarm Flow – Auto Tickets in AOTS TM
Network Alarms triggered by devices are captured by GFP (via EMS) and sent to RUBY (CC, Telco or Data/IP) for Trouble Ticket creation in AOTS-TM.
If Manual intervention is required to fix the issue, Trouble is referred to WFA/C.
AOTS TM
GFP DATA
EMS (Ciena/Juniper)
LABS (Devices)
RUBY TELCO
RUBY DATA/IP
RUBY CC
GCP

## Slide 11: IPAG SA – Application Involved
AOTS-TM: AT&T One Ticketing System-Trouble Management. AOTS-TM handles Tickets created for the troubles reported by Customer (Manual) or Network (Auto).
GCP: Global Computing Platform. GCP is the database which holds the Inventory as well as Customer related Data.
GFP-DATA: Global Fault Platform. GFP handles all the Network Alarms triggered by the devices, whenever there’s a fault in the Infrastructure.
RUBY: RUles Build by You. RUBY is a set of rules to segregate the alarms based on the device they are triggered on, and ensure a Trouble Ticket is created in AOTS-TM and assigned to the correct Work Group for resolution.
WFA/C: Work Force Allocation. WFA looks after dispatch of Field Technicians, if required for Trouble resolution.
CTP: Common Test Platform. CTP runs some predefined tests on Network Devices to isolate the Trouble reported by a Customer.
CBUS: Common BUS. CBUS is a flow through application, which handles the notification b/w AOTS and RUBY.
EBTA: EBTA. EBTA is a flow through application, which handles referral request b/w AOTS and WFA/C.
TM/BIS: Trouble Management/Business Intelligence System. TM/BIS is a flow through application, which handles referral request b/w AOTS and WFA/C.
LPP-INSTAR: Logical Provisioning Platform. LPP has access to IPAG and other CBB devices. CTP contacts LPP if it wants run tests on IPAG or CBB devices.
SQ-DATA: Trouble Management/Business Intelligence System. SQ-Data is a flow through application, which handles flow of commands and comments b/w WFA and AOTS.
WFA/DI & WFA/DO: Dispatch In & Dispatch Out. These are sub systems below WFA/C. If the trouble is on a device within CO (Central Office/Exchange), DI is engaged, else if it’s outside CO, DO is engaged.

## Slide 12
Thank You